SBC2023 – Serial data and IR remote control codes
IR protocol is NEC with a 16 bit system code and 8 bit command code. We have been testing with a common remote with a System Code of 0xef00, but we can use any other code or IR protocol that is required. We suggest that a System Code is chosen that is not in common use by other equipment.

Motion	System Code	Command Code
Continuous motion while IR is received plus preset run-on (note 1)
		Hexadecimal
Head/Backrest up	0xef00	0x04
Head/Backrest Down		0x05
Leg/Foot up		0x06
Leg/Foot down		0x07
Bed Up		0x08
Bed Down		0x09
Tilt/Trendellenburg up		0x0a
Tilt/Trendellenburg down		0x0b
Go to Preset positions (note 2)
Preset 1	0xef00	0x10
Preset 2		0x11
Preset 3		0x12
Preset 4		0x13

Programming instructions (note 3)
Learn Preset 1		0xef00	0x14
Learn Preset 2			0x15
Learn Preset 3			0x16
Learn Preset 4			0x17

System Wake-up
Wakeup (note 4)		0xef00	0x00
Stop (note 5)			0x01

Notes
1. Use with systems that just give a single command burst such as speech recognition. The motor will run for a preset time each time the command is received. A series of repeated commands might be needed to reach a desired position. These commands cannot be cancelled as they just run for a short time anyway.
2. These commands may be aborted by the Stop command, or if any IR command is received, or if any RS232 data is received.
3. Programming instructions must be received 3 times within 2 seconds to be valid and responded to.
4. This is a safety function, and the command must sent in response to the user giving a command such as “Bed wake up”. This will bring the bed control out of standby and be available for additional commands. The controller will revert to standby 60 seconds after the end of the last command. The controller LCD backlight will be active while the unit is ready for commands.
5. The STOP command will always stop any of the Move To Preset Position commands. It is not really required as any other command received when this command is active will stop all motion.

Wired serial data format
Codes sent by serial data are sent 9600 BPS, 8NE as a 4 byte sequence:
Byte 1,2 – System code MSB first
Byte 3 – Command code
Byte 4 – Checksum consisting of simple 8 bit addition of previous 3 bytes
E.g to send command “Head Up” the bytes “EF 00 04 F3” are sent.